## Slide 1: Discover Better Designs, Faster Driving Product Innovation Through Design Space Exploration
Unrestricted © Siemens AG 2016 Realize Innovation
Notes: Hello and welcome to this presentation
My name is xxx and I am the xxxx.
In this presentation we will explain what we mean with Predictive Engineering Analytics is why it’s important. We then will introduce our Simcenter portfolio, our strategy behind it and provide some examples on innovation which will be enabled by this approach.

## Slide 2: Executive Summary
The design of a solenoid assembly is a complex, and often iterative process, aimed at producing desirable force characteristics subject to available ranges for electrical and mechanical design parameters. Solenoid technology has been adopted in numerous types of industries. It is a basic part of industrial inductors, valves, security systems, etc. Although simulation has long played a key role in validating designs, its usage to discover new, higher performing, innovative designs has been limited until now.
This presentation highlights how modern simulation process automation and design space exploration can be used in a managed environment to consistently deliver high performance, low-cost designs.
An example of the design of the shape of a solenoid is used to illustrate how HEEDS MDO can be easily deployed together with standard simulation tools to help engineers discover better designs, faster!

## Slide 3: Solenoid Design Space Exploration
This study aims at increasing the force in the vertical direction on the core while decreasing the input current in the coil, while ensuring the the force remains above a critical limit
Problem Statement:
    Objective: minimize Current_Ampere
    maximize Force_Vertical_Core_Newton
    (Trade-off study)
    Constraints: Force_Vertical_Core_Newton > 40 N
Simcenter 3D CAD Model
Coil
Core
Iron Frame

## Slide 4: Solenoid Design Space Exploration
This study aims at increasing the force in the vertical direction on the core while decreasing the input current in the coil, while ensuring the the force remains above a critical limit
Problem Statement:
    Objective: minimize Current_Ampere
    maximize Force_Vertical_Core_Newton
    (Trade-off study)
    Constraints: Force_Vertical_Core_Newton > 40 N
Simcenter 3D Magnetics Model
Current
Air Volume
Flux Tangent Condition
Air Volume (mesh extrusion)

## Slide 5: Process Automation
HEEDS automates the design process with the Simcenter 3D family of solutions from CAD modification, Magnetics pre-processing, Magnetics simulation, and results interpretation, using its simple direct interface to Simcenter 3D (Simcenter 3D portal):
  CAD: HEEDS directly communicates with CAD through the exposed expressions in the CAD model
  Magnetics Pre-processing: HEEDS communicates with the Advanced Simulation module to update CAE expressions
  and updates the CAE model to reflect the
  latest CAD
  Magnetics Simulation: HEEDS directly communicates with the
  Magnetics solver to execute and extract results of the simulation
  Post Images: HEEDS automatically extracts layout states
  created in Simcenter 3D as post processing images
HEEDS MDO
Automates the CAD generation, FE pre-processing, solving and post-processing
Simcenter 3D
Updates CAD, updates CAE, executes solver, results extracted

## Slide 6: Solenoid Design Exploration Variables
Design Variable | Baseline Value | Range
Width | 1.5 | 1.5 -5.5
Thickness | 1.5 | 1.5 - 7
Current_Coil | 3 | 1 - 3
Material_Core | Steel_Sample1 | Steel_Sample1, Steel_Sample2, 416 Stainless Steel
Number_of_Turns_Coil | 1000 | 900 - 1100
Width

## Slide 7: Solenoid Design Exploration Variables
Design Variable | Baseline Value | Range
Width | 1.5 | 1.5 -5.5
Thickness | 1.5 | 1.5 - 7
Current_Coil | 3 | 1 - 3
Material_Core | Steel_Sample1 | Steel_Sample1, Steel_Sample2, 416 Stainless Steel
Number_of_Turns_Coil | 1000 | 900 - 1100
Thickness

## Slide 8: Solenoid Design Exploration Variables
Design Variable | Baseline Value | Range
Width | 1.5 | 1.5 -5.5
Thickness | 1.5 | 1.5 - 7
Current_Coil | 3 | 1 - 3
Material_Core | Steel_Sample1 | Steel_Sample1, Steel_Sample2, 416 Stainless Steel
Number_of_Turns_Coil | 1000 | 900 - 1100
Current_Coil

## Slide 9: Solenoid Design Exploration Variables
Design Variable | Baseline Value | Range
Width | 1.5 | 1.5 -5.5
Thickness | 1.5 | 1.5 - 7
Current_Coil | 3 | 1 - 3
Material_Core | Steel_Sample1 | Steel_Sample1, Steel_Sample2, 416 Stainless Steel
Number_of_Turns_Coil | 1000 | 900 - 1100
Material_Core

## Slide 10: Solenoid Design Exploration Variables
Design Variable | Baseline Value | Range
Width | 1.5 | 1.5 -5.5
Thickness | 1.5 | 1.5 - 7
Current_Coil | 3 | 1 - 3
Material_Core | Steel_Sample1 | Steel_Sample1, Steel_Sample2, 416 Stainless Steel
Number_of_Turns_Coil | 1000 | 900 - 1100
Number_of_Turns_Coil

## Slide 11: CAD Automation
A parametric CAD & Simulation model was built in NX
HEEDS drives the parametric CAD and Simulation model via the Expression Table in Simcenter 3D
HEEDS Simcenter 3D Input Portal
Locate Variables
Locate Variables

## Slide 12: CAD Automation
A parametric CAD & Simulation model was built in NX
HEEDS drives the parametric CAD and Simulation model via the Expression Table in Simcenter 3D
HEEDS Simcenter 3D Input Portal
Tag Variables in HEEDS MDO
Tag Variables in HEEDS MDO

## Slide 13: CAD Automation
A parametric CAD & Simulation model was built in NX
HEEDS drives the parametric CAD and Simulation model via the Expression Table in Simcenter 3D
Expressions Table
HEEDS Simcenter 3D Input Portal

## Slide 14: CAD Automation
A parametric CAD & Simulation model was built in NX
HEEDS drives the parametric CAD and Simulation model via the Expression Table in Simcenter 3D
Expressions Table
HEEDS Simcenter 3D Input Portal
Parametric CAD

## Slide 15: FEM Automation
Simcenter 3D’s journaling capability was utilized to update the material of the core
Journal File

## Slide 16: FEM Automation
Journal File
Simcenter 3D’s journaling capability was utilized to update the material of the core

## Slide 17: FEM Automation
Simcenter 3D’s journaling capability was utilized to update the current value in the coil
Journal File

## Slide 18: FEM Automation
Simcenter 3D’s journaling capability was utilized to update the current value in the coil
Journal File

## Slide 19: CAD Automation
Variable: Width
1.5 mm
5.5 mm
Variable: Thickness
1.5 mm
7 mm
CORE
Notes: The valid of range changes based on the value of L3

## Slide 20: Automated FE-Preprocessing
A predefined Simcenter 3D simulation file was used
  All mesh settings, physics, and solver settings were created and saved with the model
  Tetrahedral Volume Mesh ~ 200,000 elements
  Copper and Steel were assigned as materials for coil and core respectively
  Solution Time ~ 9.5 mins (4 cores)
The Simcenter automated mesh pipeline allows for the updated Simcenter 3D geometry to be swapped, the FEM model to updated, and the magnetics solution solved automatically with the Simcenter 3D portal
Automated Magnetics Solution
Automated Meshing & Boundary Condition Application
Swapping geometry

## Slide 21: Selection Recipe
A Selection Recipe was defined in the baseline sim file to capture results on the core geometry
CORE

## Slide 22: Automated Magnetics Solution
The updated Simcenter 3D magnetics simulation model is executed automatically as part of the Simcenter 3D portal execution and results extracted by HEEDS using the Simcenter 3D output portal
HEEDS Simcenter 3D Output Portal

## Slide 23: Automated Magnetics Solution
Define response extraction
HEEDS Simcenter 3D Output Portal
Tag responses in HEEDS MDO
Selection Recipe
The updated Simcenter 3D magnetics simulation model is executed automatically as part of the Simcenter 3D portal execution and results extracted by HEEDS using the Simcenter 3D output portal

## Slide 24: Automated Magnetics Solution
The average magnetic field across the core is calculated via a formula response
In order to use coil current as an objective, a formula response is defined for the current as well (= variable Current_Coil)

## Slide 25: Automated Magnetics Solution
Force on the core due to the magnetic field produced by the coil current is written out to a *.Force.txt file and the value is extracted via delimited tagging in HEEDS

## Slide 26: Automated Post Images
The Simcenter ‘Layout States’ feature was used in conjunction with the HEEDS Simcenter 3D portal to generate images to enhance the post-processing
  Layout States are created by the user in the pre-defined baseline Simcenter simulation file
  The Simcenter 3D portal automatically extracts layout states as images for each design
Macro
Simcenter
HEEDS POST

## Slide 27: Scalable Computation
300 Solenoid Designs Evaluated
  48 hrs of wall time
  ~9.5 mins per design
Design Exploration
HEEDS MDO
Windows Laptop
1 core
Simulation Execution
Simcenter 3D
Windows Laptop
4 core / job
1 concurrent job

## Slide 28: Design Exploration
Directed Modifications
Pre-Processing & Solving
HEEDS Design Exploration
CAD Modeling
Existing Design
Post-Processing

## Slide 29: Design Exploration
Directed Modifications
Pre-Processing & Solving
HEEDS Design Exploration
CAD Modeling
Existing Design
Post-Processing

## Slide 30: Design Space Exploration
74.7% Feasible Designs
0.3% Error Designs
25% Infeasible Designs
Baseline (Starting) Design
Pareto Front Family of Best Designs
GOAL
GOAL

## Slide 31: Design Space Exploration – Pareto Front
Baseline (Feasible)
Current_Ampere = 3 A
Force_Vertical_Core_Newtons= 96 N
GOAL
GOAL

## Slide 32: Design Space Exploration – Pareto Front
Design ID:291
Current_Ampere = 2.18 A (27.3 )
Force_Vertical_Core_Newtons= 112.7 N(17.4% )
GOAL
GOAL
All percentages marked are with respect to the baseline design

## Slide 33: Design Space Exploration – Pareto Front
Design ID:271
Current_Ampere = 2.52 A(16% )
Force_Vertical_Core_Newtons= 217.5 N(127% )
GOAL
GOAL
All percentages marked are with respect to the baseline design

## Slide 34: Design Space Exploration – Pareto Front
Design ID:269
Current_Ampere = 2.84 A (5.3% )
Force_Vertical_Core_Newtons= 263.3 N(175% )
GOAL
GOAL
All percentages marked are with respect to the baseline design

## Slide 35: Design Space Exploration – Pareto Front
Design ID:90
Current_Ampere = 3 A (0%)
Force_Vertical_Core_Newtons= 293.6 N(206% )
GOAL
GOAL
All percentages marked are with respect to the baseline design

## Slide 36
Assess Design Trends – Parallel Plot
Current_Ampere
Force_Vertical
Core_Newtons
Number_of Turns_Coil
Width
Thickness
1
3
293.6
0
1100
900
5.5
1.5
1.5
7
1
3
416 Stainless Steel
Steel_Sample1
Current_Coil
Material
Steel_Sample2
Objectives
Constraint
Design Variables
Maximize
Minimize
HEEDS is using 300 evaluations to efficiently search for good designs in a landscape of ~28 million possibilities
**Note : Current_Ampere = Current_Coil

## Slide 37
Number_of Turns_Coil
Width
Thickness
1
3
293.6
0
1100
900
5.5
1.5
1.5
7
1
3
416 Stainless Steel
Steel_Sample1
Current_Coil
Material
Steel_Sample2
Force_Vertical
Core_Newtons
Current_Ampere
Assess Design Trends – Parallel Plot

## Slide 38
Number_of Turns_Coil
Width
Thickness
1
3
293.6
0
1100
900
5.5
1.5
1.5
7
1
3
416 Stainless Steel
Steel_Sample1
Current_Coil
Material
Steel_Sample2
Force_Vertical
Core_Newtons
Number of turns in the coil seems to have tight tolerancing around the upper limit of its range
Current_Ampere
Assess Design Trends – Parallel Plot

## Slide 39
Number_of Turns_Coil
Width
Thickness
1
3
293.6
0
1100
900
5.5
1.5
1.5
7
1
3
416 Stainless Steel
Steel_Sample1
Current_Coil
Material
Steel_Sample2
Force_Vertical
Core_Newtons
Thickness of the core lies in the upper half of its variable range
Current_Ampere
Assess Design Trends – Parallel Plot

## Slide 40
Number_of Turns_Coil
Width
Thickness
1
3
293.6
0
1100
900
5.5
1.5
1.5
7
1
3
416 Stainless Steel
Steel_Sample1
Current_Coil
Material
Steel_Sample2
Force_Vertical
Core_Newtons
Pareto front designs include only two materials for the core
Current_Ampere
Assess Design Trends – Parallel Plot

## Slide 41: Assessing Design Trends – 2D Relation Plot
FEASIBLE

## Slide 42: Assessing Design Trends – 2D Relation Plot
Steel_Sample1
In the Feasible design set, Steel_Sample2 seems to be the most preferred material for the core
Steel_Sample2
416 Stainless Steel

## Slide 43: Assessing Design Trends – 2D Relation Plot
Steel_Sample1
Steel_Sample2
The trend seem to continue on the Pareto front as Steel_Sample2 being the most preferred material

## Slide 44: Assessing Design Trends – 2D Relation Plot
0.55 T
1.38 T
Average_Magnetic_FluxDensity_Core_Tesla
FEASIBLE DESIGNS WITH STEEL_SAMPLE2 AS MATERIAL
Force on the core increase with an increase in the average magnetic flux density in the core

## Slide 45: Assessing Design Trends – Plot Views
Average_Magnetic_Flux Density_Core_Tesla
0.7 T
1.35 T
Steel_Sample2
On the Pareto front, force on the core and current in the coil shows a strong positive correlation with average magnetic flux density in the core

## Slide 46: Assessing Design Trends – Plot Views
Average_Magnetic_Flux Density_Core_Tesla
On the Pareto front, unlike thickness, width of the core seems to trend the same way as average magnetic flux density in the core hence positively correlated to force on the core and current in the coil
0.7 T
1.35 T

## Slide 47: Results Versus Objectives
Demonstrated CAD-embedded automated workflow to simplify virtual prototype construction
  CAD: NX (automatically vary 3D geometry)
  Magnetics: Simcenter 3D (prepare model / perform magnetics analysis)
Scalable Computation
Demonstrated that scalable computation hardware and software can be effectively used to accelerate virtual prototype testing
  300 designs successfully evaluated in 48 hours
Intelligent
search
Efficient Exploration
Proved that intelligent search can help engineers to discover better designs, faster
  Discovered a non-intuitive design that showed 127% increase in the force on core with 16% reduction in the coil current than the baseline design in under 300 evaluations
  Identified critical design variables and their relationship to performance metrics for the solenoid
automated
workflow
Process Automation